## Slide 1: Lab4 – 7-segment driver
2018/10/19
Sun Wen-Lin

## Slide 2: Lab4 Requirements
一個七段顯示器的driver
  將writer所寫入的指令轉換為七段顯示器的顯示資訊
  當reader讀取時提供最新顯示資訊
一隻Writer的程式
  將參數每個三秒寫入一次device
  每次write一個指令(e.g. A)
  ./writer 1234567890abcdefABCDEFgggg

## Slide 3: 助教已完成部分
Reader – socket client
  對device做read
  期望會拿到七段顯示器的顯示資訊，一個長度為7的陣列Array
  Array[0]代表a段亮(1)/暗(0), Array[1]代表b段亮(1)/暗(0), …
  將顯示資訊透過socket傳給server
  ./reader [server_ip] [port] [device_path] &
  “&” 代表背景執行，欲將其回到前景則輸入指令 fg
Seg.py – socket server
  當作七段顯示器
  透過socket接收reader所傳來之七段顯示器顯示資訊

## Slide 4: Network configuration with ip tool
Enable Network interface
  ip link set eth0 up
Set ip address
  ip addr add [ip]/24 dev eth0
Set default route
  ip route add default via [gw_ip]
Others
  https://www.tecmint.com/ip-command-examples/

## Slide 5: Run Seg.py
Install python2.7
  sudo apt-get install python2.7
Install tkinter
  sudo apt-get install python-tk
Run
  python seg.py [port]

## Slide 6: Tftp on ZC702
Get a file from remote tftp server
  tftp –g –r [filename] [server_ip]

## Slide 7: Data copy between kernel and user space
copy_from_user(void* to, const void __user * from, unsigned long n)
  Copy a block of data from user space
copy_to_user(void __user * to, const void * from, unsigned long n)
  Copy a block of data into user space

## Slide 8: Hints
Add option “--static” when you compile
Driver需要定義的operation: read, write
Demo SOP:
  板子: insmod, mknod
  VM: python seg.py [port(8888)]
  板子: ./reader [ip] [port(8888)] [device_path] &
  板子: ./writer [testcases]

## Slide 9
static char map[16] = {
0b1111110, // 0
0b0110000, // 1
0b1101101, // 2
0b1111001, // 3
0b0110011, // 4
0b1011011, // 5
0b1011111, // 6
0b1110000, // 7
0b1111111, // 8
0b1111011, // 9
0b1110111, // A,a
0b0011111, // B,b
0b1001110, // C,c
0b0111101, // D,d
0b1001111, // E,e
0b1000111 // F,f
};
七段顯示器顯示資訊表